## Slide 1: DuraMax
Presenter’s name
High-performance motors
June 22, 2021

## Slide 2
Highly engineered and fully modeled motor offering
Increased operational envelope
Robust and durable
Multi-run capable tools
Modern motor solution
Copyright 2020 Baker Hughes Company. All rights reserved. 81664
Notes: Going forward we want to flip this around and
Standardize to a high load capable design that can be re-run multiple times with minimal effort
As well as be quickly configured into any service level
Higher CE, reduced inventory, reduced GBV, reduced R&M cost, higher FM and returns
1-2-1 Vision
Automation, automation, automation
  Automatic programming, BHA build
  Automatic deck testing, tool programming, tool verification
  Automatic configuration of telemetry, automatic telemetry synchronization
  Automatic reporting and update of performance recording data bases
  Auto Self-Diagnostics of 121 Platform components support re-run decisions
  One button log generation
  Reduces training needs for FSEs, reduced number of FSEs

## Slide 3
Optimized power sections
New contours
Improved efficiency
Robust elastomer offerings for all mud types
Higher durability and robustness
Ground up re-design
Modern engineering
DuraMax motor increased operational envelope
High build rate capability and rotating limits
High strength components
High strength AKO
High WOB capability
High load and long life bearings
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 4
New Rotor catcher
New contour layout:
Optimized for DOWNHOLE performance
Novel R/S-Fit concept
High flow capable (360gpm)
15% more torque
40% more power output
New stator tube design:
Stronger Baker Hughes proprietary connections
Larger tube ID supporting highest performance power sections
Wear protection
at conections
Field proven elastomer options
Design overview: Optimized power sections
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 5
Flexible stabilization options
HIGH TORQUE CAPABLE DRIVE TRAIN:
Designed to withstand stall torque of strongest power sections
Vibration resistant design
High load capable bearing assembly:
High WOB up to 180kN / 40 klbs
Short BTB
Withstands highest bit side loads
Improved ako design:
Baker Hughes proprietary thread design
Withstands highest bending loads
Foolproof AKO scribeline (Angle reading = high side)
Design overview: Lower end
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 6
Specifications | 
Short bit-to-bend | 4.1 ft
High load, long life PDC bearings | 40 klbs WOB
Increased flow rate | 360 gpm
Increased torque output (ft-lb) | +15%
Increased power output (HP) | +35%
Available power sections | 
Pre-contoured | 1.00 rpg, 5/6, 13 stage
Pre-contoured | 0.75 rpg, 5/6. 9.5 stage
Conventional | 0.75 rpg, 5/6, 9.5 stage
Conventional | 0.50 rpg, 5/6, 6.5 stage
5-1/8-in. DuraMax motor platform
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 7
D100-5130C
DuraMax
Revolutions per gallon (RPG)
Implied decimal after the first number
i.e. 100 = 1.00 rpg; 075= 0.75 rpg
Number of lobes (rotor)
implies 5/6 lobe geometry
Number of stages
Implied decimal after the second number
i.e. 130 = 13.0 stages; 065 = 6.5 stages
Power section
C = Conventional
P = Pre-contoured
DuraMax motor nomenclature
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 8
Size | Nomenclature | Description
5-1/8 | D100-5130P | 1.00 revolutions per gallon, 5/6 rotor/stator, 13 stages, Pre-contoured stator
5-1/8 | D75-5095P | 0.75 revolutions per gallon, 5/6 rotor/stator, 9.5 stages, Pre-contoured stator
5-1/8 | D50-5065P | 0.50 revolutions per gallon, 5/6 rotor/stator, 6.5 stages, Pre-contoured stator
5-1/8 | D100-5130C | 1.00 revolutions per gallon, 5/6 rotor/stator, 13 stages, Conventional stator
5-1/8 | D75-5095C | 0.75 revolutions per gallon, 5/6 rotor/stator, 9.5 stages, Conventional stator
5-1/8 | D50-5065C | 0.50 revolutions per gallon, 5/6 rotor/stator, 6.5 stages, Conventional stator
5-1/8 | D25-5030C | 0.25 revolutions per gallon, 5/6 rotor/stator, 3 stages, Conventional stator
DuraMax motor nomenclature examples
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 9
5-1/8-in. D100-5130P
RPG: 1.00
Stages: 13.0
Flow Rate: 105 – 360 gpm
Diff. Pressure: 2,685 psi
5-1/8-in. D075-5095P
RPG: 0.75
Stages: 9.50
Flow Rate: 105 – 360 gpm
Diff. Pressure: 1,965 psi
Op. Power: 405 hp
Op. Torque: 5,780 ft-lbs
Max. Power: 540 hp
Max. Torque: 7,685 ft-lbs
Op. Power: 295 hp
Op. Torque: 5,770 ft-lbs
Max. Power: 395 hp
Max. Torque: 7,675 ft-lbs
Pre-contoured power section
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 10
RPG: 0.75
Stages: 9.50
Flow Rate: 105 – 360 gpm
Diff. Pressure: 1,965 psi
RPG: 0.50
Stages: 6.50
Flow Rate: 105 – 360 gpm
Diff. Pressure: 1,785 psi
Op. Power: 260 hp
Op. Torque: 5,050 ft-lbs
Max. Power: 345 hp
Max. Torque: 6,715 ft-lbs
Op. Power: 175 hp
Op. Torque: 5,095 ft-lbs
Max. Power: 235 hp
Max. Torque: 6,775 ft-lbs
Conventional power section
5-1/8-in. D75-5095C
5-1/8-in. D50-5065C
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 11
D100-5130C
DuraMax
Revolutions per gallon (RPG)
Implied decimal after the first number
i.e. 100 = 1.00 rpg; 075= 0.75 rpg
Number of lobes (rotor)
implies 5/6 lobe geometry
Number of stages
Implied decimal after the second number
i.e. 130 = 13.0 stages; 065 = 6.5 stages
Power section
C = Conventional
P = Pre-contoured
DuraMax motor nomenclature
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 12
Size | Nomenclature | Description
5-1/8 | D100-5130P | 1.00 revolutions per gallon, 5/6 rotor/stator, 13 stages, Pre-contoured stator
5-1/8 | D75-5095P | 0.75 revolutions per gallon, 5/6 rotor/stator, 9.5 stages, Pre-contoured stator
5-1/8 | D50-5065P | 0.50 revolutions per gallon, 5/6 rotor/stator, 6.5 stages, Pre-contoured stator
5-1/8 | D100-5130C | 1.00 revolutions per gallon, 5/6 rotor/stator, 13 stages, Conventional stator
5-1/8 | D75-5095C | 0.75 revolutions per gallon, 5/6 rotor/stator, 9.5 stages, Conventional stator
5-1/8 | D50-5065C | 0.50 revolutions per gallon, 5/6 rotor/stator, 6.5 stages, Conventional stator
5-1/8 | D25-5030C | 0.25 revolutions per gallon, 5/6 rotor/stator, 3 stages, Conventional stator
DuraMax motor nomenclature examples
Copyright 2020 Baker Hughes Company. All rights reserved. 81664

## Slide 13
(AS OF MID-APRIL 2019)
>650,000
FEET DRILLED AND
116 RUNS
30%
FASTER CURVE
13 DEG./100 FT
>10KFT / 46 HRS.
FASTEST LATERAL DRILLED
36
SINGLE RUN
TD~9k-10k FT
DOUBLE DISTANCE DRILLED
PER DAY IN PERMIAN
SECOND FASTEST
LATERAL ON FIRST RUN
+25%-40%
ROP
WITH EASY AND
CONSISTENT
TF CONTROL
EFFICIENT SLIDING
Rockies (Bakken, Three Forks, Powder River Basin), Permain (Wolfcamp A, B, Lower Sprayberry), and Canada
Rockies (Bakken, Three Forks, Powder River Basin), Permain (Wolfcamp A, B, Lower Sprayberry), and Canada
Copyright 2020 Baker Hughes Company. All rights reserved. 81664
DuraMax high-performance motors
Notes: As of mid-April; Rockies (Bakken, Three Forks, Powder River Basin); Permian (Wolfcamp A, B, Lower Sprayberry); Canada
116 Runs
>650,000 ft. drilled
7,000 CH; 5,700 DH

## Slide 14
Case study: Williston Basin, North Dakota
5 1/8-in. DuraMax motor
DRILLED
DRILLING HOURS
10,294 FT.
LATERAL IN
46
LOW VIBRATION
FOOTPRINT AND
SMOOTH POWER
DELIVERY
FASTEST
DRILLED
LATERAL
FOR CUSTOMER
DRILLING DAYS
SAVED
3.3
Chart: Lateral section days vs depth
Copyright 2020 Baker Hughes Company. All rights reserved. 81664
Notes: Published
The Challenges
Drill 6” lateral section in single run
Minimize sliding for well path corrections
Minimize vibrations to avoid MWD failures
Consistent power delivery to avoid Bit failure or wear out
Baker Hughes solution
5 1/8” DuraMax D75-5095P

## Slide 15
Case study: Midland County, Texas, Wolfcamp A
5 1/8-in. DuraMax motor
DRILLED
DRILLING HOURS
7,652 FT. IN
80
114 FT./HR ROP
MAINTAINED
DELIVERED
CONSISTENT
BURN IN CURVE
OF RIG TIME
SAVED
3 DAYS
3,127
OF DAILY FOOTAGE
ACHIEVED
FEET PER DAY
Copyright 2020 Baker Hughes Company. All rights reserved. 81664
Notes: The Challenges
Comparison of Motor technologies
Drill curve @10deg./100ft. BUR
Drill 6 ¾” lateral section
Baker Hughes solution
5 1/8” DuraMax D75-5095C

## Slide 16
Case study: Midland County, Texas
5 1/8-in. DuraMax motor
ONE-RUN
TO TOTAL DEPTH
LATERAL
INCREASE
OVERALL ROP
17.1%
IN AVERAGE
DRILLED
DRILLING HOURS
9,529 FT.
LATERAL IN
145
INCREASE
FOOTAGE/DAY
9.5%
IN AVERAGE
MAINTAINED ROP
65
FEET PER HOUR
Copyright 2020 Baker Hughes Company. All rights reserved. 81664
Notes: Published
The Challenges
Drill 6 ¾” lateral section to TD in single run
Formation push
Baker Hughes solution
5 1/8” DuraMax D50-5065C & Dynamus extended-life PDC drill bit